Status of the MAPS project
Imperial College 27.03.2007
Y. Mikami, O. Miller, V. Rajovic, N.K. Watson, J.A. Wilson
University of Birmingham
Mark Thomson
University of Cambridge
J.A. Ballin, P.D. Dauncey, A.-M. Magnan, M. Noy
Imperial College London
J.P. Crooks, M. Stanitzki, K.D. Stefanov, R. Turchetta, M. Tyndel, E.G. Villani
Rutherford Appleton Laboratory

---
Overview
Introduction
Status
  - Sensor Design
  - Sensor Simulation
  - DAQ/Testing
  - Detector Simulations
Next steps

---
Introduction
Development of an alternative readout sensor for the CALICE ECAL
“Swap-In” Solution leaving mechanical structure untouched
Use of MAPS with high granularity and digital readout

---
What are MAPS ?
Monolithic Active Pixel Sensors
Integration of Sensor and Readout Electronics
Manufactured in Standard CMOS process
Collects charge mainly by diffusion
Development started in the mid-nineties, now a mature technology

---
Hybrid Pixels and MAPS
MAPS
LHC-style
Hybrid Pixel
sensor
Pixels
Bump
Bonds
Readout Electronics

---
MAPS in Detail
Electronics
MAPS architecture:
Sensor and the electronics are integrated in one wafer
Charge Collection mainly in epi-layer
Charge collected mostly due to diffusion
Incoming
particle
Diodes
Epi-Layer
(up to 20 µm)
CMOS
Wafer (~700 µm)

---
The CALICE MAPS
For the CALICE ECAL a specific MAPS was designed:
Pixel Size (50 x 50 µ)
Binary Readout (1 bit ADC realized as Comparator)
4 Diodes for Charge Collection
13 bit Time Stamping
Hit buffering for entire bunch train
Capability to mask individual pixels
Threshold adjustment for each pixel

---
A new process technology
Simulation showed, that the n-wells absorb a lot of charge (hence affecting the signal)
We isolated the n-well with a “deep p-well” implant (3 µm thick)
Novel INMAPS process used for the CALICE MAPS
Electronics
Deep p-well
Incoming particle
Diodes
Epi
CMOS
Wafer

---
Sensor Electronics
Two types of pixel readout
Shaper & Sample
Average deadtime (~600 ns/ 450 ns )
Simulation shows similar noise characteristics
Both share the Comparator design
Having two readout architectures allows us to explore several ideas at once

---
The two pixels
Pre-Shaper
Pre-Sampler
Rst
Vrst
Preamp
PreRst
Buffer
s.f
Cfb
Cin
Buffer
s.f
Vth+
Vth-
Reset
Sample
Cstore
--ns
Preamp
Shaper
Rst
Cpre
Cfb
Rfb
Rin
Cin
Vth+
Vth-

---
The Pixel
50x50 µm size
0.18 µm process
12 µm Epi-layer
Deep p-wells
5 metal layers
224 1.8 V transistors
1 3.3 V transistor
36 capacitors

---
The test sensor (V1.0)
42 pixels
5 pixels
Consists of 42x84 pixels
Has a logic strip for
  - 5 pixels wide
  - Hit buffering using SRAM technology
  - Time stamping (13 bit)
  - Configuration registers
  - the only part with Clock lines
Logic strip is a “dead area” for particle detection
(~ 11 % inefficiency)
Pixels
Logic Strip
84 pixels

---
The test structure (V1.0)
Pre-Sample
Architecture
Wafer
Pre-Shaper
Architecture
Area for test structures

---
Sensor Simulation
We are using Centaurus TCAD to simulate the sensor
Using CADENCE GDS file for pixel description
Simulate diodes from adjacent pixels for charge sharing effects
Detailed Pixel performance studies
  - Collection Efficiency
  - Charge Collection Time
  - Signal/Noise

---
Diode placement
Classical problem
  - Place n circles in a square
  - No analytical solution
Only 4 Diodes as a starter
Mathematics faces reality
  - Constraints due to Design Rules
  - Electronics
  - Space
Numerical Solution
50 µm
Charge Collection Efficiency

---
The setup
Diodes
Electronics
Adjacent
Diodes
Bias:
n-Well 1.8/1V
Diodes: 1.5V
Epi-Layer
Substrate

---
Simulation Setup
7 Hit Points simulated
1 µm distance

---
Charge Collection
Charge collected
Distance to Diode (µm)
Charge (e-)
Collection Time
Distance to Diode (µm)
Time (ns)
Main parameter to vary is Diode Size
ILC Bunch spacing ~ 300 ns

---
Signal/Noise
Signal/Noise
Distance to Diode (µm)
S/N
*N.B. S/N 0.9µm N = 16 e-
Signal to Noise > 15 for 1.8 µm Diode Size
*N.B. S/N 1.8µm N = 16.5 e-
*N.B. S/N 3.6µm N = 21.3 e-

---
MAPS DAQ & Testing
Development of DAQ board and firmware has started
Complete test setup foreseen
  - Cosmics
  - Sources
  - Laser
  - Test beam

---
RAL Laser Test setup
Powerful Laser setup
1064, 532 and 355 nm Wavelength
Accurate focusing
(<2 µm)
50 Hz Repetition rate
Fully automatized
Will be used to test the CALICE MAPS

---
Detector Simulation
Implementation of the MAPS into GEANT/MOKKA
  - Patched MOKKA 6.02
50x50 µm pixel size
15 µm “Active Area” (Epi-layer)
Detector Model used LDC01(Sc)
ECAL with 30 layers
  - 20 layers 2.1 mm Tungsten
  - 10 layers 4.2 mm Tungsten
Charge diffusion and thresholds are implemented in a separate “Digitization” step

---
Shower Shapes
GEANT4 : One 20 GeV Electron shot along y-axis

---
Spatial resolution in x
Impact of B field
Moliere Radius
GEANT4 :20 GeV Electrons shot along y-axis

---
Linear Response
Linear response for electrons up to 400 GeV
GEANT4 level without charge diffusion

---
Resolution
Good resolution over wide energy range
GEANT4 level without charge diffusion

---
Noise Occupancy
Noise for 2880 bunches
Vary noise probability
With Noise=O(10-6)
  - P=0.3 % for 1 hit per pixel
  - P=0.0004 % for 2 hit per pixel
But O(1012) pixels !
  - ~3 109 single hits
  - ~4 106 double hits
  - ~0 triple hits

---
Charge sharing algorithm
Sum energy in
50x50 μm² cells
Esum
Apply charge spread
Eafter charge spread
Geant4 Einit
in 5x5 μm² cells
Add noise to signal hits
with σ = 90 eV
(1 e- ~ 3 eV  30e- noise)
+ noise only hits
prob. 10-6  ~ 106 hits in the whole detector
BUT in
a 1 cm² tower : ~30 hits in 30 layers.
Register the position and the number of hits above threshold
%Einit
%Einit
%Einit
%Einit
%Einit
%Einit
%Einit
%Einit
Einit

---
First results
Algorithm depends on accurate simulation input from Centaurus
First results shows algorithm work nicely
Does not take into account deep p-well yet
Will be updated with the latest pixel simulations and noise estimates

---
Basic Hit Clustering
Number of neighbours
3 or 4
Total : 11 or 12,
instead of 37.
x
Hit Clustering
Loop over hits classified by number of neighbors
Number of neighbors < 8 :
count only 1 (or 2 for last 10 layers) and discard the neighbors
8 neighbors AND one of the neighbor has 8 neighbors :
count 2 (or 4) and discard the neighbors

---
Particle Flow
Extending PandoraPFA to handle Digital ECAL hits
First development version is running
Lots of things to improve
  - Calibration of MAPS response is critical
  - Optimize clustering for MAPS
  - Particle ID needs modifications
  - Take advantage of MAPS resolution
σE/√E 0.36+0.01 for
Z->uds at 91 GeV
in the ECAL barrel

---
Design Issues
Pixel parameters
  - Pixel size
  - Number of Diodes / Diode size
PCB/Readout Chips
Module structure
Cooling
Manufacturing
Cost

---
Pixel parameters
MAPS Pixels improve spatial resolution/granularity
by a factor of ~ 1000 compared to analog pad ECAL
Lower pixel size is set by size of the integrated electronics (lower boundary of 50 µm)
Upper bound set by charge collection time/efficiency and multiple hits
No fixed upper bound, reasonable value is around 100 µm
Best performance found with 4 diodes and 1.8 µm diode size

---
PCB/ Readout Chip
All the electronics is integrated within the the sensor
No need for
  - Complicated PCB design
  - Dedicated Readout Chip
Still needs to provide Power/Clocks/Commands to the MAPS
Can be done by “Stave Controller” at the end of the Stave

---
Stave Structure
MAPS can be used as swap-in solution without alterations to the mechanical design (Baseline)
One can also take further use of MAPS benefits

---
How it could look like
Take advantage of MAPS benefits
Lack of hybrids/ASIC allow less complex/thinner PCB
Thinner sensors (down to 100 µm)
Bump-bond MAPS
MAPS
Stave Controller
with optical link
PCB
Tungsten

---
Cooling
Cooling for the ECAL is a general issue
Power Savings due to Duty Cycle (1%)
Target Value for baseline ECAL 4 µW/mm2
Current Consumption of MAPS ECAL: 60 µW/mm2 depending on pixel technology
Compared to analog pad ECAL
  - Factor 1000 more Channels
  - Factor 10 more power
Advantage: Heat load is spread evenly

---
Manufacturing & Costs
Less complex structure due to lack of VFE ASIC
Need for large scale process (2000-3000 m2)
CMOS is an industry standard process
Many foundries can do it
CMOS wafers are readily available
CMOS is ~2 cheaper than “HEP-style” silicon

---
What happens next ?
Submit Sensor V1.0 Mid April
Sensor V1.0 due back Mid July
Improve/enhance GEANT simulation
Testing Sensor V1.0
Do physics analyses with a MAPS based ECAL
Improve sensor simulation with data from V1.0
Design Sensor V2.0 using all the experience made with V1.0
Submit Sensor V2.0

---
Summary
MAPS effort is advancing well
Sensor V1.0 is almost done
Simulation of MAPS based ECAL made huge progress
Still quite some challenges ahead
Interested to work on MAPS ? Contact us !
Thanks to everyone in the MAPS group for their help in preparing the talk

---
Backup

---
Beam background
Owen ?

---
Cooling cont'd
Channels
Power (W)

---
MAPS vs Baseline

---
Dead area
We need 5 dead pixels every ~42 sensitive pixels (under study) for the pixels logic.
σ(E)/E = α/√E
α = 0.1561 asymptotical value
α = 0.161 @ 42 sensitive pixels
3 % increase : we can live
with that !!

---
DAQ data volume
Physics rate is not the limiting factor
Beam background and Noise will dominate
Assuming 2880 bunches and 25 bits per Hit
  - 106 Noise hits per bunch
  - ~O(1000) Hits from Beam background per bunch (estimated)
Per bunch train
  - ~9 Gigabyte Data
  - Readout Required 41 GB/s
  - CDF SVX-II can do 18 GB/s already