MC Production and Reconstruction
Summary and Plans
Valeria Bartsch, Fabrizio Salvatore,
A.-M. Magnan, and Nigel Watson

---
The Monte Carlo chain, from beam to reconstructed hits
Beam profile
Gaussian
@ first order
Realistic simulation of the beam line material
BDSIM
setup of H6 beam line
Geant4 ParticleGun
+ beam spread
Calice geometry
Input configuration parameters
+ list of corresponding data runs
Mokka
Internal geometry
File Run1
File RunN
....
Noise, calibration constants,...
Reconstruction
Reco File Run1
....
Analysis
Reco File RunN

---
First MC Production
1- Give a unique identifier to each configuration: in order to easely recombine reconstructed files (MC and DATA) for analysis.
2- Create and fill a nominalConfiguration folder in the Calice database, containing all the parameters per run that are not already there
3- TAG database before any production
4- Define a list of runs, get all the parameters from the database in a flat file, one line per run.
5- Execute bash script to create Mokka steering and macro files from the flat configuration file.
6- Grid submission
7- Scripts to automatize jobs output, retrieve output statistics (and write it somewhere??)
Configuration :
default (=nominal) values
Energy, angle, beam parameters,
detector model,
ECAL, HCAL, TCMT pos w.r.t. (0,0,0)
Cerenkov pressure and gas
particle PDG ID
Statistics factor
List of runs associated

---
Iterations
Going from nominal to real values:
  - Create a second folder realConfiguration. Unique identifier ?? and fill database with measured values.
  - In the script creating the configuration flat file from the list of runs, specify a flag to know which folder should be used per run: real or nominal ?
  - Re-use bash script to create corresponding Mokka steering and macro files.
Information needed in Mokka output: one integer (run number) and one string (database tag) in the runHeader.

---
Reconstruction and Geometry problem
Mokka
SimCalorimeterHit
Raw data
noise
SimpleHitSearch
TBEcalDigitisation
RawCalorimeterHits
Position from Mokka database
= no position for noise only hits
Position from Calice database
= no position for unconnected modules
Temporary solution ???
Solution 1) Mokka needs to output a GEAR xml file & GEAR needs to be extended to describe the detailed geometry of the prototype
Iterations (software ? Regeneration ?) necessary to obtain the same position as in the data.
CalibrateAndApplyThreshold
Solution 2) Extend the position table to all modules + use Calice database to generate the Mokka driver.
CalorimeterHits

---
Conclusion
Mokka production will start ASAP with nominal parameters, and should be completed in the timescale of the next reprocessing of the data.
Will need manpower to fill the database with missing values for all runs.
Lots of iterations to find the real values and feedback to MC: need to be organised !!
Data need to be reconstructed before MC, e.g. to fill the noise in the database.
Reconstruction code is being finalized : POSITION ISSUE STILL NOT SORTED. No good solution, which one is less worse ??? My feeling: Calice database position, and discarding hits in unconnected layers. HCAL reconstruction uses Calice database position.... TCMT? Tracking ?

---
Thank you for your attention