TPAC 1.X 55Fe results
Marcel Stanitzki
RAL 16.01.2009

---
Some details about 55Fe
Gamma and X-ray radiation:
        Energy (keV) Intensity (%)
XR l	0.64	0.66 % 10
XR kα2	5.888	8.2 % 4
XR kα1	5.899	16.2 % 7
XR kβ3	6.49	0.96 % 5
XR kβ1	6.49	1.89 % 9

---
Spectrum from Konstantin

---
Analog pixel scans
- Done with TPAC 1.2 (old data sets with 1.1 as well)
- Two data sets each
  - -30 mV Threshold (entire spectrum)
  - -120 mv Threshold (tail)
- There is a 1/0.81 gain correction (only applied if explicitly stated)
- Using a fixed setup now
  - takes ~ 3 days for one pixel
  - 150 GB of data
- Available data sets
  - see https://heplnm061.pp.rl.ac.uk/display/spider/TPAC+55Fe+Spectra

---
Fit models
- For the 120 mV data set
  - Exponential+Crystal Ball (Kα) +Gauss (Kβ)
  - Crystal Ball
- For the 30 mv data set
  - Exponential +Gauss (FakePeak) + Gauss(Kα)
  - Kα has two low stats to be sensitive in this data set
- New fitter using RooFit (much better ...)

---
TPAC 1.2 +DPW 12 μm
Fitted Values
Crystal Barrel FKT for K_alpha
     ka_mean : 205.918 0.22371385
    ka_sigma : 4.6170221 0.20512349
    ka_alpha : 1.2884144 0.13555629
        ka_n : 0.0026548376 0.083639886
Gauss for K_beta
     kb_mean : 227.73171 0.70361675
    kb_sigma : 3.3479737 0.65209354
Exponential Background
   exp_coeff : -0.040348041 0.0019318991

---
More on ...
K_beta/K_alpha Ratio observed :1.105934
K_beta/K_alpha Ratio expected :1.0975309
K_alpha :205.918 corrected:254.21975 mV
K_alpha width:4.6170221 corrected:5.7000273 mV
K_beta :227.73171 corrected:281.15026 mV
K_beta width :3.3479737 corrected:4.1333008 mV
---------------
Gain from K_alpha mV/e:0.15692577
Gain from K_beta mV/e:0.15812726
Noise from K_alpha mV :5.7000273
Noise from K_beta mV :4.1333008
Noise from K_alpha e :36.323079
Noise from K_beta e :26.139079
Applying 1/0.81 correction

---
Fake peak
Fitted Values
Gauss for the Fake peak
     fp_mean : 58.601428 0.35430359
    fp_sigma : 8.8903209 0.3239019
Gauss for K_alpha
     ka_mean : 196.49425 1.9331505
    ka_sigma : 10 0.12398403
Exponential Background
   exp_coeff : -0.047306252 0.0017584892
Fake peak :58.601428 corrected:72.347442 mV
Fake peak width :8.8903209 corrected:10.975705 mV
---------------

---
Stitching
- Trying to combine both spectra …
- This is still beta
  - more stable normalization
  - check errors again
- Using same model as for the Fake peaks
- Trying to derive fractions of fake-peak to real peak

---
“Stitched Spectrum”
Fake peak fraction :0.61345738
K_alpha fraction :0.0034473355
Ratio :0.0056195192

---
TPAC 1.2 highres 12 μm
Fitted Values
Crystal Barrel FKT for K_alpha
     ka_mean : 200.2132 0.34410319
    ka_sigma : 4.6019026 0.27889855
    ka_alpha : 0.39205586 0.097359728
        ka_n : 0.41106072 0.17457918
Gauss for K_beta
     kb_mean : 220.17943 0.60013773
    kb_sigma : 3.5907866 0.48640374
Exponential Background
   exp_coeff : -0.063199093 0.0016797816

---
More on ...
K_beta/K_alpha Ratio observed :1.0997248
K_beta/K_alpha Ratio expected :1.0975309
K_alpha :200.2132 corrected:247.17679 mV
K_alpha width:4.6019026 corrected:5.6813612 mV
K_beta :220.17943 corrected:271.82645 mV
K_beta width :3.5907866 corrected:4.4330699 mV
---------------
Gain from K_alpha mV/e:0.15257826
Gain from K_beta mV/e:0.15288327
Noise from K_alpha mV :5.6813612
Noise from K_beta mV :4.4330699
Noise from K_alpha e :37.235718
Noise from K_beta e :28.996436
Applying 1/0.81 correction

---
Fake peak
Fitted Values
Gauss for the Fake peak
     fp_mean : 98.910429 0.16926532
    fp_sigma : 9.6201518 0.22942849
Gauss for K_alpha
     ka_mean : 199.53495 0.85862334
    ka_sigma : 2.450916 0.66738968
Exponential Background
   exp_coeff : -0.030080472 0.00028527005
Fake peak :98.910429 corrected:122.11164 mV
Fake peak width :9.6201518 corrected:11.876731 mV
---------------

---
“Stitched Spectrum”
Fake peak fraction :0.34395865
K_alpha fraction :0.0016250091
Ratio :0.0047244316

---
TPAC 1.2 highres 18 μm

---
TPAC 1.1 -DPW 12 μm (old)
Fitted Values
Crystal Barrel FKT for K_alpha
     ka_mean : 207.32391 0.11780295
    ka_sigma : 3.9058313 0.11532728
    ka_alpha : 1.1355633 0.048686145
        ka_n : 0.093029556 0.020265332
Gauss for K_beta
     kb_mean : 223.88193 0.28681614
    kb_sigma : 3.7272012 0.22738122
Exponential Background
   exp_coeff : -0.0456119 0.0017876693

---
More on ...
K_beta/K_alpha Ratio observed :1.0798655
K_beta/K_alpha Ratio expected :1.0975309
K_alpha :207.32391 corrected:255.95545 mV
K_alpha width:3.9058313 corrected:4.8220139 mV
K_beta :223.88193 corrected:276.39745 mV
K_beta width :3.7272012 corrected:4.601483 mV
Gain from K_alpha mV/e:0.15799719
Gain from K_beta mV/e:0.15545413
Noise from K_alpha mV :4.8220139
Noise from K_beta mV :4.601483
Noise from K_alpha e :30.519618
Noise from K_beta e :29.600262
Applying 1/0.81 correction

---
Summary
- Gain with correction is
  - 153-157 mV (corrected)
- Noise is
  - 30-37 electrons
- Kα is between
  - 200-208 mV (not corrected)
- Kβ is between
  - 220-227 mV (not corrected)
- Fake peak vary widely (we expect that)

---
TPAC 1.0
Sensor 13

---
TPAC 1.0 (cont)

---
TPAC 1.1
Sensor 25 untrimmed

---
So ...
- Fake peak 12 μm +DPW
  - 72.3 mV (analog)
  - 165 TU (bulk)
  - 1 mV =2.3 TU (1 TU = 0.44 mV)
- Noise then (including comparator)
  - Width of Peak is 7.2 TU (from the fit ...)
  - That is 3.2 mV (or 20.4 electrons)
  - however, the fake peak isn't infinitely small

---
Fake peak width
- Is about 11 mV (corrected)
- Noise the same for both fake and Kα
  - Width of fake peak ~ 9.4 mV
  - that is 21.6 TU
- Using that
  - much larger than measured peak width
  - to be revisited ...

---
Some other items

---
Upshot
- Calibrating with the fake peak is still tricky
- Analog test pixel performance is very consistent with simulation
- Bulk is still mystery